1. Explanation of the work carried out by the beneficiaries and Overview of the progress

- Created opensource software repository “eucall-software”
- Implemented generic simulation platform “simex_platform” to integrate various simulation tools and interfaces for their use and communication.
- Developed and integrated simulation codes and/or respective interfaces for
  - Propagation of coherent x-ray pulses through beamline optics based on wavefront propagation
  - Source and beamline simulation for synchrotron radiation based on x-ray tracing
  - Photon-matter interaction with molecules,
  - Photon-matter interaction with plasmas created by high-power optical laser irradiation
  - Photon-matter interaction with warm dense matter created by high-energy optical laser irradiation
  - Scattering from molecules
  - Scattering from plasmas
  - Simulation of 2D area pixel detector signal via “Poissonization” of scattered intensity
  - Orientation of 2D diffraction patterns into 3D diffraction volumes
  - Reconstruction of 3D electron density distribution from 3D diffraction volumes
- Performance optimization of
  - Wavefront propagation code SRW
  - Molecule scattering code SingFEL
- Deployment of simulation platform via Source archive, binary package, docker container.
- Identified promising areas of application and scientific explorations:
  - Single-particle imaging with x-ray free electron lasers and optimization of experimental parameters
  - Scattering diagnostics of plasma instabilities after short-pulse laser-plasma interaction
  - Absorption and scattering diagnostics of warm dense matter and optimization of pump laser pulse shapes
  - Possibilities of laser-plasma based electron acceleration and coherent light sources

1.2 Explanation of the work carried per WP

1.2.1 Work Package 4

Task 4.1.1: X-ray optics and beam propagation
XFEL:The simulation module for x-ray optics and propagation of coherent x-ray pulses in
x-ray free electron laser beamlines is complete. It utilizes "WavePropaGator" (WPG), a python
interface library to the state-of-the-art wavefront propagation code "Synchrotron Radiation
Workshop" (SRW). SIMEX provides a "Calculator" (scriptable python user interface) to the WPG library
utilities and predefined WPG beamline definitions for the SPB-SFX instrument at
the European XFEL. Further beamlines for XFEL or other FEL facilities can easily be added if needed.

WPG has the capability to read in precomputed x-ray pulse data from the XFEL pulse database XPD [].
Propagated wavefronts are stored in the same format at XPD entries, facilitating the data transfer.
In order to provide a more generic data interface, WPG output can optionally be reformatted to
comlply with the openPMD metadata standard used e.g. by the particle-in-cell code PIConGPU []. The
latter is used for short pulsed optical laser-matter interaction in SIMEX and other codes.

ESRF: The simulation module for X-ray optics and beam propagation for the ESRF is realised using the OASYS (OrAnge SYnchrotron Suite) software [Rio et al. Proc. SPIE 9209, p. 9209X (2014) ], an open source graphical user interface (GUI) based on Orange 3. OASYS includes ShadowOui, which is the OASYS interface for the shadow3 ray tracing open source software.

The workflow consists of graphical modules that can be inserted onto the workspace; which represents the synchrotron beamline and all its optics. At the ESRF, we now have a workspace that has been developed to simulate the ID24 beamline (X-ray absorption studies) where the first dynamic compression experiments (long pulse laser-matter interactions) will be carried out ESRF. Graphs can be generated within the GUI to display X-ray properties at any point in the workflow. Once the whole beamline optics have been simulated (and the X-ray source has been chosen), all the relevant information from the simulation can be passed to other SIMEX platforms by running a python script directly in OASYS.
The python script is called at the end of the OASYS simulation to initiate the HydrocodeInputWriter calculator, passing it the relevant information required to determine (and make suggestions to) the required target parameters based on the users desired request before running the hydrocode simulations with expected laser conditions. This has a direct influence on task 4.1.2 (sample-photon interaction) and code is currently being developed to pass this information from one simulation to the next and to provide the user with the key information to make an informed decision on the experimental parameters for laser-matter interactions.

Task 4.1.2: Sample-photon interaction
XFEL: We employ the code suite XRAYPAC [Z. Jurek et al., Journal of Applied Crystallography, vol. 49, no. 3, pp. 1048–1056 (2016)] to model interaction of coherent ultra-intense x-ray pulses
with atomic and molecular samples, e.g. biomolecules for coherent imaging applications (single
particle imaging). The code is developed and maintained at the Center for Free Electron Laser
Science (CFEL).

XRAYPAC reads the output of the wavefront propagation module and a file that contains the
initial atomic structure of the sample (atomic species and cartesian coordinates of each atom.) It
calculates the atomic structure and the electron density distribution as a function of time taking
into account the interaction with the external FEL field. This data is stored at defined intervals
("snapshots").

Execution of XRAYPAC requires a license. The licensing process took longer than anticipated which
delayed the integration into SIMEX. A demo version of XRAYPAC, as exists in simS2E Yoon et al., Scientific Reports, vol. 6, p. 24791, (2016), can be run
through SIMEX, using the same data formats for in- and output. An interface to the full version of
XRAYPAC will be developed as soon as the code becomes available. In the meantime, data from the wavefront propagation must be sent via network to the XRAYPACK developers at CFEL. XRAYPACK results are then sent back to the SIMEX user for further processing
(scattering calculations).

HZDR:We simulate the interaction ultrashort ultraintense lasers with solid matter using the Particle-In-Cell (PIC) code PIConGPU. It solves Maxwell’s equations on a grid with ions and electrons treated as clouds of charged particles. The code is open source and published under GNU GPL on github.com. It is under constant development with regular releases and since recently also features first methods to extend its applicability towards solid-density targets. For interaction with other modules of SIMEX we implemented standardized input and output in openPMD format. The output can therefore serve as input for FEL- or scattering simulations like our in-house ParaTAXIS project. We started implementing photon transport and interaction with the sample through atomic physics by generalizing the particle model to carry additional information about the states of the particles within the particle cloud it resembles, e.g. electronic level populations.

ESRF: The laser-matter interactions are modelled with 1D radiation hydrodynamics computer codes. We employ the code Esther [Colombier et al., Phys. Rev. B, vol. 71, no. 16, p. 165406 (2005)], developed by the CÉA France, to model the interaction between long-pulse high energy lasers and sample target packages. The license to use Esther must be obtained by requesting (via email) academic use for the program from the authors.
To integrate the modeling requirement of SIMEX to pass between two subsequent Calculators, we have developed interface modules to interact with Esther. The main module creates the input file required to run the hydrocode. This takes both the requested parameters from the user (target sample and laser properties) as well as any information passed from the X-ray tracing simulations.

ELI: In this work at ELI-ALPS, the possibility of amplifying the low intensity ultra-short (≤fs) pulses using as intermediate amplifying medium by using resonant backward Raman amplification (BRA); such pulses are anticipated to get produced in the form of the secondary sources at ALPS (Attosecond Light Pulse Source) center of ELI (Extreme Light Infrastructure). In preliminary assessment of the scheme, the analytical expressions for the pump/seed laser pulses and characteristic features are obtained which concisely describe the parameter regime of resonant BRA applicability in achieving significant amplification. The consistency of the scheme in the context of ELI-ALPS sources has been validated through particle in cell simulations. The peak intensity of the amplified seed pulse predicted via simulation results is found in reasonable agreement with the analytical estimates. Utilizing these analytical expressions as a basis in perspective of ELI-ALPS parameter access, a specific example displaying the key and laser parameters for amplifying weak seed pulse has been configured; the limitations and conceivable remedies in resonant BRA implementation have also been highlighted.
Related publication: S. K. Mishra and A. Andreev, Physics of Plasmas 23, 083108 (2016).

Task 4.1.3: Scattering signal simulation
XFEL: Two scattering codes are developed and maintained by XFEL: "singFEL" for scattering from finite
systems (atoms, molecules, clusters), and "XRTS" for scattering from plasmas. Both are fully
integrated into SIMEX, allowing to setup and execute simulations using a generic scriptable user
interface. The data format has been designed such that both applications can read the results from
the beamline propagation.

singFEL reads the snapshots from the photon-matter interaction calculation, the scattering geometry
(detector position, size, and pixels), and the intensity distribution in the sample interaction
plane resulting from the beamline propagation. From this input data, it computes the scattered intensity in each detector pixel as a
function of time and the integrated signal. This serves as input for a detector simulation.

XRTS calculates a scattering spectrum for given plasma parameters (density and temperature) and scattering geometry. The source spectrum and the detector point spread function
are convoluted with the scattering spectrum. In a next step, integration over density- and
temperature profiles, taken e.g. from optical laser-plasma interaction calculations, will be added
as a feature to SIMEX.

ELI: In deviation from the proposal, the simulations of scattering from short-pulse laser produced plasmas, as simulated by PIC, will be implemented and performed by HZDR, not by ELI.

HZDR: We developed a scattering code ParaTAXIS running on GPUs that adds the capability to SIMEX to simulate the X-ray photon scattering in short-pulse laser generated plasmas. It takes input from SIMEX' X-ray generation and propagation in openPMD format and converts the X-ray wavefronts to photons in a particle interpretation. It is hence fully integrated in the SIMEX platform. The photons are then traced through the plasma (plasma data read from an offline PIC simulation) and are scattered on electron and ion density and propagated further. The correct phase relation of the photons is kept to allow for coherent superposition later at the detector. Development is ongoing in order to implement more scattering channels in a next step.

Task 4.1.4: Detection
XFEL:
Simulations of the detector response to incoming scattered radiation is handled in two qualitatively different ways at XFEL:
1.) Poissonization only: The calculated distribution of scattered intensity in the detector plane is converted into a distribution of scattered photons per detector pixel. To mimic the poissonian counting statistics of pixel detectors, this photon distribution is convolved with a Poisson distribution at each pixel.
2.) Detailed detector simulation: The x-ray camera simulation toolkit X-CSIT [Joy et al., Journal of Instrumentation, vol. 10, no. 4, pp. C04022–C04022, (2015)] allows detailed detector simulations including particle creation, charge transport, and, due to a recent extension [IEEE Conference Proceedings of the Nuclear Science Symposium 2015], electronics of real detectors. Integration of X-CSIT into SIMEX is complicated by the dependency of the extensions on Karabo, the European XFEL data handling and controls framework. Both Karabo and X-CSIT are under heavy development. Only very recently, X-CSIT has been updated to comply with the latest release of Karabo, such that it could now also be integrated into SIMEX. Already now, it is possible to feed singFEL data into a standalone version of X-CSIT (i.e. independent of SIMEX) and hand the resulting data back to the SIMEX toolchain thanks to already defined data interfaces.

ESRF: For X-ray absorption experiments at the ESRF, one of the critical components of the target package is the sample thickness for the particular k-edge of the sample being studied. This determines the XAS jump and has a large impact on data quality. One aspect of the hydrocode simulations from ESRF is to perform a loop function to optimise the sample thickness based on the expected flux (from X-ray source simulations) and the minimum / maximum sample thickness based on the hydrocode wave interactions.
The XAFS signal reflects the local order of the shock compressed matter and can be simulated by combining first principle electronic structure methods with linear response theory. A well-known implementation is the non-open source code FEFF [Rehr et al., Comptes Rendus Physique, vol. 10, no. 6, pp. 548–559 (2009)].
To enhance and extract further relevant information from the hydrocode simulations, the particle velocity can be extracted from the hydro opmd files, at the sample / window interface, to show the expected VISAR signal (velocimetry diagnostic traditionally used in long pulse shock experiments to determine pressure).

Detailed modeling of the x-ray detector, as for XFEL, is not foreseen. Absorption spectra simulated by FEFF will be convoluted with a detector point spread function and source bandwidth.

ELI: Detector modeling for ELI specific applications will re-use the tools and concepts developed at XFEL, such that a separate detector modeling activity at ELI is not required. Instead, ELI (ALPS) will concentrate on the simulations of novel x-ray source concepts based on Laser-Wakefield Electron Acceleration, see Sec.3.

Milestone 4.1:
Milestone 4.1 demonstrates that all aforementioned simulation modules are operable. The Milestone document lists the definition of used data interfaces and provides details about the simulation codes.

Task 4.2.1 First example
XFEL: As a first application of the SIMEX simulation platform, we performed a start-to-end simulation of a single-particle imaging experiment using ultra-short 3 fs pulses of 5 keV XFEL photons focussed onto a 7 nm sized biomolecule (PDB entry 2NIP). The diffracted radiation is captured in a 2D pixel area detector. Results of this study have been submitted for publication [C. Fortmann-Grote et al. “Start-to-end simulation of single particle imaging using ultra-short pulses at the European X-ray Free Electron Laser”.

ESRF: The integrated radiation-hydrodynamics simulation capabilities were used to optimize the drive laser pulse profile in a hypothetic dynamic compression experiment with Iron targets. This documentation of this study will be provided to SIMEX users as an online tutorial. This is currently in preparation.

Task 4.2.2 Generalized simulations
ESRF: The integrated radiation-hydrodynamics simulation capabilities were used to optimize the drive laser pulse profile in a hypothetic dynamic compression experiment with Iron targets.
Here, the (optical) photon-matter interaction was modeled with radiation-hydrodynamics simulations. Documentation of this study will be provided to SIMEX users as an online tutorial. This is currently in preparation. The next step will be to couple the rad-hydro simulations with a simulation of the x-ray probe (ESRF synchrotron), described by the x-ray raytracing method and simulations of the x-ray absorption fine structure signal using electronic structure calculations and the FEFF code.

HZDR: Work is ongoing to produce a synthetic diffraction pattern from hot and dense plasmas excited by a short-pulse optical laser and probed by coherent x-ray photons delivered from the European XFEL. The x-ray field is simulated by coherent wavefront propagation, while the optical photon-matter interaction is simulated by PIC codes. Diffraction (scattering) is described by the paraTAXIS code. All codes are part of the SIMEX repository.

Task 4.3.1 Test and validate modules and workflow, including HPC workflow
DESY: Work at DESY has focussed predominantly on adapting the simulation codes used in SIMEX
for use on HPC platforms where this was not already the case. In particular, the code SRW for coherent wavefront propagation has been upgraded to benefit from shared-memory parallelism using the OpenMP framework. Secondly, a SRW version compiled with MPI allows processing of many x-ray source fields in parallel, which speeds up sampling of source fluctuations.
Running SIMEX on HPC platforms is facilitated by a mechanism in the python layer of simex_platform that identifies the HPC resources (number of CPU cores, number of nodes) semi-automatically and sets the batch execution parameters accordingly.
The detector simulation code X-CSIT has been upgraded to be compatible with the recent Karabo release and is now ready for integration and use in SIMEX.

XFEL: We have started to assess the validity of single-particle imaging simulations by benchmarking our simulation results against experimental data from RDV virus diffraction data collected at LCLS, Stanford, USA.

Task 4.3.2: HPC, data management, and data analysis
DESY: Work has started to develop a web-based simulation platform as a service to users by exposing the simex_platform user interfaces through a web-based graphical user interface.

XFEL: We are currently consolidating common data analysis tasks in virtual diffraction experiments in an object-oriented programming approach. Similar to “Calculators”, abstract interfaces for simulation codes, “Analyzers” encapsulate data analysis tasks like image plotting, projections, integrations and statistical analysis. Our open platform will allow and facilitate integration of established data analysis codes into SIMEX and usage of SIMEX simulations and analysis e.g. in the XFEL data analysis framework “Karabo”.

1.3 Impact

SIMEX contributes to the development of technical components and solutions required for all facilities via the development of common user and data interfaces to and between advanced simulation codes for start-to-end simulation of ESFRI facility experiments. All developed software is thoroughly documented, occasionally, documentation of (re-)used pre-existing software is complemented. Exchange of ideas, concepts, results, and documentation mainly functions via the code repository at www.github.com/eucall-software. All software developed in SIMEX is open source licensed, thus available to all users and interested persons in and outside of EUCALL. Documented data formats, specified in SIMEX and in SIMEX RIs as well as format conversion utilities between SIMEX formats and other, common formats in use in certain research communities enhance the inter-operability between EUCALL RIs and other RIs, projects, and individual researchers.

2. Update of the data management plan (if applicable)

N/A.

3. Deviations from Proposal (if applicable)

The deviations from the EUCALL proposal is adopted to extend its relevance and applicability; subsequently to offer the extended SIMEX platform to users of worldwide light source facility. The ‘laser plasma accelerator based coherent light source’ is a near future challenge to several big accelerator facilities / institute eg LBNL (USA), RAL (UK) and latest research organisation eg EuPRAXIA; who looks future in substituting the ‘big and high cost’ conventional accelerator with ‘compact and economic’ ‘plasma accelerator’. Thus it’s a great deal of proposal to extend (or deviate) the development of SIMEX platform in order to investigate the simulation research on ‘laser plasma accelerator based coherent light source’.

As a novel application for SIMEX platform, it is planned and under development to simulate a laser-plasma accelerator based free electron laser by feeding the output of the PIC simulation, i.e. the phase space distribution of accelerated electrons into a FEL simulation code to investigate the possibility of laser based FELs with realistic electron bunch properties.

In continuation of SIMEX development project, we propose to develop start-to-end simulation software for experiment towards the realization of laser plasma accelerator (LPA) based coherent light source (FELs). Since the conventional accelerator has the limit of the gradient due to the structure surface field limit, the best gradient achieved now is less than 100MeV/m. LPA will be the next generation accelerator facilities with the ultrahigh gradient which will reach 100GeV/m. Due to the ultra-high gradient of LPA, the accelerator facility will be miniaturized greatly. Development of SIMEX platform will offer us to investigate the suitability of laser plasma accelerators as a source of high quality electron beam instead of linear accelerators (LINACs) which are very large and expensive facilities.
     Regarding this simulation development, we (Dr. A. Sharma and Prof. A. Andreev, ELI-ALPS) initiated the project in collaboration with Dr. C. Fortmann-Grote (XFEL Hamburg) from 13th February 2017, which was initially discussed during the EUCALL Annual Meeting, HZDR Dresden. The main task in this project is to enable the simulation of LPA based coherent light sources (FELs) by coupling a particle-in-cell (PIC) code that describes the LPA to a FEL simulation code (GENESIS). During the XFEL visit (13th Feb. - 17th Feb. 2017); we developed a python calculator which combines the PIC simulation output (using PIConGPU code) to the FEL simulation code as an input electron beam as shown below in sketch diagram.

Thereafter electron beam data generated from the LPA simulation was readable to the FEL simulation code GENESIS to study it further a source of coherent radiation. The current form of simulation software needs further advancement to enable the optimization of focusing optics, magnetic chicane, magnetic undulator and radiation undulator; to minimize the input data during the execution of SIMEX.
SIMEX development for LPA driven FELs may offer the route for compact and economic XFEL instruments which is in contrast to the large-scale facilities build worldwide based on radiofrequency technology acceleration which require hundred meter long undulator and kilometer long accelerating lines.

3.1 Tasks

In line with the aforementioned deviation from the proposal, ELI's contribution to the detector simulations (Task 4.1.4) have not been fulfilled.
The detector simulation software X-CSIT with extension for XFEL detectors has only become available in a form suitable for integration into SIMEX. Hence, this item has not been completed in Task 4.1.4 and detector simulations have to be performed “offline”.

4. Critical Risks

4.1 The following “Foreseen Risk” was defined for WP4:

Software developed at different locations not interoperable

The following “Risk Mitigation Measure” was defined for WP4:

Clear communication and definitions of interfaces.

Project Period: October 2015 – March 2017

This risk materialized. From the outset, only few codes where interoperable. We adopted an open data format description (openPMD) to mitigate this obstacle.

 4.2 The following “Foreseen Risk” was defined for WP4:

Failure of a partner to meet an obligation

The following “Risk Mitigation Measure” was defined for WP4:

Responsibilities and work well defined, similar expertise can be allocated in the consortium, regular reporting on status of progress in EB

Project Period: October 2015 – March 2017

Did this Risk Materialise? No

4.3 Have any unforeseen risks arisen during the Project Period: October 2015 – March 2017?

Insert text here (max. 1 page)

5. Innovation

How many prototypes have been developed within your Workpackage? ____ (Number)

How many Testing Activities (feasibility/demo) have been performed? ____ (Number)

Will your activities lead to launching any of the following into the market?

New product (good or service) YES/NO

New process YES/NO

New method YES/NO

	What the term means (for your report)
Innovation	The introduction within a firm or market of a new or significantly improved: / product (good or service) / process / marketing method / organisational method (business practices, workplace organisation or external relations) / The minimum requirement for an innovation is that the product, process, marketing method or organisational method must be new (or significantly improved) to the firm.
Prototype, testing activities	Proof of S&T feasibility: Results of innovation activities that confirm/verify the technical feasibility of new products and processes in a (near) operational environment. Includes: / prototypes & demonstrations of new products and processes / results of testing/piloting with users / trial production and pilot plants in manufacturing / trials & testing for services, such as how new technologies affect provision or how significant improvements in existing services perform
Clinical trials	Systematic tests on human volunteers to ensure that new drugs, vaccines or treatments are both safe and effective and can be introduced to the market.
Product	Good or service introduced to the market or to the company/organisation what is new or significantly improved in its capabilities, usability, components or sub-systems. Goods include packaged & downloadable software/music/film.
Process	Production process, distribution method or supporting activity that was implemented within an organisation.
Method	Refers to organisational method or marketing concept/strategy in business/organisational practices (including knowledge management). / organisational method - covers workplace organisation or external relations not previously used by your enterprise/organisation / marketing method - significant changes in product design or packaging, product placement, product promotion or pricing that have not been used before

Appendix 1: Full description of EUCALL Objectives – Section 1.1 of EUCALL proposal
O1 Analyze and promote the efficient use of ALL-RIs

Information on user demand versus availability of beamlines and equipment (“overbooking”) will be collected and analysed. Limitations restricting the optimum use of the infrastructures and the optimum response to user demands will be identified. Some of the existing networks have already implemented network-wide access policies designed to address and remove such limitations. Strategies for the removal of limitations, considering the combined portfolio of facilities/beamlines within this project, will be investigated and promoted. Strategies towards a “joint access policy” will be developed and will be practically investigated. Coordinated training of users and management, as a measure to promote strategies for more efficient RI use, will be investigated.

O2 Identify and develop the combined research potential

Information of the research potential versus technical specifications will be compiled into a suitable “super matrix”, allowing the identification and analysis of duplications and missing elements, or new research opportunities arising from the combination of offers by different RIs. EUCALL will support, monitor, and analyze prototype experiments based on the combined use of advanced optical and accelerator-based lasers. Here, the employment of state-of-the-art devices with unprecedented specifications on both sides presents significant and new challenges. Best practices will be identified and disseminated throughout the consortium. It will be explored how such initiatives can be better stimulated.

O3 Analyze and promote the innovation potential offered by the ensemble of ALL-RIs

An analysis of the innovation potential of the individual RIs, but more importantly of the potential following from their combination, will be performed and used to develop and recommend strategies for effective exploitation. Developments of specific activities to promote innovative technological and scientific developments will be based on this analysis. Recommendations will be established in collaboration with industry liaison officers of the partners, and including input from the major national and international stakeholders. Finally active promotion of the results among the stakeholders will occur.

O4 Identify joint foresight topics in science and research policy, further strengthening the portfolio of advanced laser light source RIs within the ERA

Involving joint user communities, facility operators, political stakeholders, and funding agencies the identification of foresight topics shall be performed in terms of unique and complementary instrumentation directions, new research opportunities, and novel science and innovation potentials with societal dimension. This new potential is enabled through the (combined) use of the ALL-RIs, and the activities will mainly be performed through workshops and expert round tables involving the respective stakeholder groups.

The next four, more technical objectives are of common and urgent need to the ensemble of ALL-RIs, but also present excellent cases in which the cross-community cooperation of partners with largely complementary background will contribute to find new and original solutions to specific technical challenges. These specific joint development activities therefore serve as first examples for the development of cross-cutting services and the optimization of the RIs addressed by the synergy activities of EUCALL.

O5 Development and implementation of a simulation platform

The challenging scientific goals, the often complex experimental schemes, and the high oversub- scription of advanced laser light source RIs—coupled with a user community using different types of experiment installations—require tools to efficiently prepare proposals and experiments, and to enable the best use of valuable facility time. One such tool is to simulate experiments in order to predict or validate experiments and scientific results, or assist in optimally planning the use of valuable beamtime. The development and implementation of a modular simulation platform will enable users and RI operators to create sophisticated simulations of a wide breadth of experiments using the various advanced laser RIs.

O6 Development of ultrafast data acquisition

The high repetition rates of the laser light sources and the need for a most efficient usage of facility time at the RIs leads to the urgent need of higher performance and ultrafast data acquisition techniques. In particular, the inspection of experimental results requires the and analysis of data at the time of collection (online). Given the complexity of data acquisition systems, this leads to the requirement for high-performance computing capabilities close to data taking systems. Furthermore, the bandwidth of data acquisition systems and the need to optimize the use of data acquisition and storage installations leads to a need to validate data as early as possible in the data acquisition chain in order to enable rejection of invalid data. Specific developments address the development of Field Programmable Gate Array (FPGA) and Graphics Processing Unit (GPU) programming as part of the data acquisition chain for online processing of data, quality enhancement, data compression and treatment techniques (e.g. image and pulse analysis, vetoing, selection, correlation), and of high-speed data interfaces and injection techniques to allow online processing and transfer to subsequent analysis and storage clusters.

O7 Development of sample handling and positioning systems

High repetition rate laser facilities offer new possibilities to study laser-matter interaction processes across a wide parameter range and overcome low count-rate limitations. While the light sources provide such high repetition rate, systems for the quick and precise manipulation of samples into the laser beam require urgent attention. Each light source has systems for sample replacement, however, so far no attempt has been made to unify the necessary steps of sample characterization and positioning with the aim of giving external user groups a service for a more efficient conduct of experiments and interoperability between facilities. An integrated concept for decentralized sample characterization and fast sample positioning at the participating facilities will be developed.

O8 Joint development of advanced diagnostics

All ALL-RIs produce intense, ultrashort X-ray pulses whose properties may vary from pulse to pulse. To operate these sources, control the pulse parameters, and perform quantitative experiments it is therefore essential to measure the X-ray light pulse properties shot-to-shot and—if possible—in a way that does not noticeably alter the pulses. The development of suitable diagnostics devices and methodology for the key parameters of pulse energy, shape of the wave front, and exact arrival time is indispensable for all facilities. Techniques originally developed by the two light source communities for different parameter ranges will be adapted to the wavelength range, pulse energies and repetition rates of the individual facilities, and thus made commonly available.

Appendix 2 – WP4 Description

Objectives
The challenging scientific goals, the often complex experimental schemes, and the high oversubscription of advanced laser light sources—coupled with a user community using different types of experiment installations—require tools to efficiently prepare proposals and experiments, and to enable the best use of valuable beamtime. One such tool is to simulate experiments in order to predict or validate experiments and scientific results. The key objective of SIMEX is to develop and implement a simulation platform enabling users and RI operators to fully simulate experiments using the various advanced laser RIs. This simulation explicitly accounts for the coherent and, where
applicable, ultrashort (femto- and atto-second) nature of the radiation.

Description of work
The development and implementation of a simulation platform is based on contributions by all participating partners. European XFEL is coordinating this WP due to its extensive previous work in this area. Three major tasks have been defined within this WP. The first addresses individual modules to simulate specific physical processes relating to parts of the overall experiment. Here, the different partners enter with their core expertise and can address specifically their problems and applications. Planned contributions are modules for imaging of weakly scattering biomolecules (European XFEL), of density modulations following laser–matter interaction (HZDR, ELI), and of dynamically compressed matter similar to planetary cores (ESRF). Additional modules addressing different problems could be created by further RI operators or users groups inside or outside EUCALL. The modules are connected via a common interface protocol. This protocol allows the integration of modules from different sources and with differing purposes into the overall platform. A second task is to apply the platform, first to example cases and later to generalized problems. The third task concerns the technical implementation with eventually large compute requests and a modular structure of the software. All of these tasks are explicitly open to additional contributions by users or further RI operators. The WP makes explicit use of the specific know-how and background by the different RIs
to include modules reflecting the physical properties encountered in these specific conditions. Likewise, this expertise will become available to all RIs and for the user programs. Open-source programming makes this effort accessible to the user community and the output of these simulations– modelled scattering data can also be used for testing or benchmarking the algorithms developed in WP5 (UFDAC). Innovation aspects include the commercialization of these simulation tools and the commercialization of hardware solutions.

Task 4.1: Delivery of individual simulation modules and common interfaces for interoperability
(all)
Different “modules” of simulation are required for a “source to signal” simulation, including numerical propagation of radiation, description of the photon–matter interaction (in different physical regimes), and the scattering of radiation from a sample to a detector.

Task 4.1.1: X-ray optics and beam propagation (XFEL, ESRF)
Simulation of coherent and partially coherent X-ray beams propagating through X-ray optical systems to produce accurate estimates of the focal spots of such systems, including the structure of these focal spots.

Task 4.1.2: Sample-photon interaction (XFEL, HZDR, ESRF, ELI)
Sample-photon interaction: Simulation of the sample-photon interaction and the diffraction signal that different samples (single particles, nanocrystals, plasmas–including atomic physics processes) produce from such interactions with both longer nano-, and pico-second pulses, as well as shorter femto- and atto-second pulses.

Task 4.1.3: Scattering signal simulation (XFEL, ELI)
Calculation of ideal scattering signal from a sample as described in Task 4.1.2.

Task 4.1.4: Detection (all)
Investigation of the processes involved in full simulation of advanced X-ray detectors for future workflow integration.

Task 4.2: Simulation from source to signal (all)

Task 4.2.1: First example (XFEL, all)
An initial example simulation using one source model, one propagation module, one type of photon– matter interaction and one type of scattering model is a necessary step in the definition of intermodule interfaces and as a precursor to a generalised simulation. For this first example, an X-ray free-electron laser source, focusing X-ray optics, a photon–matter interaction with a biomolecule and an ideal signal at a detector will be modelled.

Task 4.2.2: Generalized simulation(s) (all)
As per Task 4.2.1, simulations will now be carried out using several different models of photon–matter interaction and scattering. The generalized simulation includes different X-ray sources (XFELs, plasmas, etc), different propagation (focusing, divergent, ray tracing, or coherent wave), different photon–matter interaction (radiation damage in biosamples, plasmas, shock waves in matter) and signal generation from optically “thin” and “thick” samples.

Task 4.3: Test and validate modules and workflow, including HPC workflow (DESY, all)

Task 4.3.1: Benchmarking, testing, and cross validation
Benchmarking, testing, and cross validation of simulation workflows against each other and—where
possible—measured data.

Task 4.3.2: HPC, data management, and data analysis
Provide a framework towards a service to users to optimize their experiment setup (pre-experiment)
and data analysis (post-experiment) as well as archive, publish, and share simulations, including
negative results.

Deliverables
D4.1: Design report and advanced photon-matter simulation software –short pulses (M12) D4.2: Design report and advanced photon-matter simulation software –long pulses (M12) D4.3: Interoperability of simulation workflows (M24)
D4.4: Generation of simulated coherent scattering data from plasma and non-plasma samples (M24)
D4.5: Testing, validation, and example workflow (M36)

Milestones
M4.1: Single modules operable (M12)
M4.2: First example simulation (M24)
M4.3: Simulations interoperable (M24)
M4.4: Tested and documented simulation code (M36)

Appendix 3: Full description of EUCALL Expected Impact – Section 2.1 of EUCALL proposal
Red text is highlighted as particularly relevant to WP4,5,6,7.
The EUCALL proposal is the beginning of a completely new level of collaboration between the two types of advanced laser light sources in Europe. Through the comprehensive cooperation it will support the ongoing implementation of the involved ESFRI projects and prepare the grounds for a most efficient and comprehensive exploitation of the enormous research and innovation potential of the whole ensemble of advanced laser light source installations in Europe.

EUCALL will contribute to the expected impact set out in the work programme as follows:

Contribution to the realisation of the Innovation Union flagship initiative's Commitment n. 5:
“to complete or launch the construction of 60% of the ESFRI projects by 2015”; saving of resources

The joint development of technical components and solutions that are required for all facilities will make sure that the complementary know-how existing in the consortium is shared and the most suitable solutions are implemented at all facilities in an efficient way. Together with the actions planned to develop, promote, and implement strategies towards optimum combined use of the ALL- RIs, including user operation, harmonized access policies and training, this work will support the efficient implementation and start of user operation of the ESFRI facilities. As all these activities promote efficiency, they will also contribute significantly to saving resources.

Common ready-to-use services, systems, standards or other types of components will be made available to the involved research infrastructures initiatives, including the non-ESFRI projects, thus contributing to the development of a consistent European research infrastructures ecosystem.

It is the intention of the project to initiate a comprehensive cooperation in all relevant areas of common interest, including technology development, science applications, optimum use of the cluster RIs, harmonized access policies and optimum exploitation of their science and innovation potential. In addition, the cluster consortium is well-defined and comprises all European ALL-RIs and the associated networks. Therefore EUCALL will have a strong impact on the development of a consistent European RI ecosystem in this field, extending even beyond into and connecting with the wider optical laser and synchrotron radiation RI networks.

Interoperability between research infrastructure services, including data services, enables novel
research leading to innovation and new insights;

Interoperability of EUCALL RIs is a specific goal of WP3 SYNERGY in order to use the complementary ensemble of RIs in the most efficient way. In addition, the technical work packages will considerably enhance interoperability by developing standard solutions for the simulation of experiments, sample handling, data services and photon diagnostics. This will enable researchers to use a combination of different instruments and services at different RIs for their research without significant additional effort, thus widening the research potential and leading potentially to novel applications and innovation. At the same time, it will lead to a merging of the traditional user communities and, together with other measures planned under WP3, to the attraction of new user communities and a higher success rate of their new projects.

The efficiency and productivity of researchers rise thanks to an easier and seamless access to complementary services provided by different infrastructures and/or to reliable and open data services and infrastructures for discovering, accessing, and reusing data;

The comprehensive approach to interoperability of the facility services throughout the EUCALL RIs together with harmonized access policies and common strategies for enhancing and optimizing complementarities of the characteristic features of the RIs and the experimental stations and services they provide, will dramatically enhance the efficiency and productivity of researchers and, hence, ensure the most efficient use of the ensemble of RIs.

Improving innovation capacity

As described above, improved interoperability between the different RIs and their services will considerably enhance the capacity for research and potential innovation. One Task of WP3 focuses specifically on strategies how to exploit the research for innovation, based on experience available in the consortium. This will result in a more efficient transfer of research results to commercial products and services and will also enhance the level of support for and cooperation with industry.

Other important impacts

The comprehensive cooperation attempted by the EUCALL project is unprecedented in the world and will significantly contribute to Europe’s competitiveness and leadership in terms of research and
innovation capacity.

Appendix 4: Mid-Term Report Timeline

12 December 2016: WPLs receive templates for Mid-Term Report (Technical part).
12 December 2016: WPLs are briefed on the requirements of the Technical part of Mid-Term Report at Executive Board meeting
31 March 2017: Deadline for WPLs to submit completed Technical parts to Coordinator
21 April 2017: Deadline for beneficiaries to submit the Financial Reporting (Form C and Use of the Resources) to the Coordinator
30 April 2017: Deadline for draft of Completed Technical Report sent to partners, to be returned within 10 days
10 May 2017: Completed Technical part sent to EUCALL Director
30 May 2017: Deadline for submission of entire Mid-Term Report to European Commission.